## Slide 1: Adapting the Home for Wheeled Mobility
Frazier Rehab Institute
Spinal Cord Medicine Program

## Slide 2: What does being at home mean to you?
Each of us has ideas of what we need in a home…
  Security and safety
  Privacy
  Convenience
  A place to heal
A place to eat, sleep, bathe, come and go, and do usual daily tasks as easily as possible
  Feel comfortable and able to relax with others
  Able to communicate and be understood & accepted

## Slide 3: Adapting the Home
It’s time to start talking about it
  What do you need to know
  What are your resources?
  How do you get started?

## Slide 4: Adapting the Home
See examples of:
Ramps
Bathrooms
Living Area
Kitchens
Outdoor Living
Let’s start with Ramps

## Slide 5: Getting in/out of the house with a wheelchair
The American with Disabilities Act (ADA) encourages use of a 1:12 ramp… commonly seen in public spaces
  1:12 means: to climb 1”, use 12” of ramp
  A 1:12 is safer for walkers and is within the ability of a manual wheelchair rider or someone pushing a wheelchair
  To ramp a rise of 5”, use 5’/feet of ramp for a 1:12 ramp
  To ramp a rise of 14”, use 14‘/feet of ramp for a ramp
A good resource:
  http://www.wikihow.com/Build-a-Wheelchair-Ramp

## Slide 6: Getting in/out of the house with a wheelchair
Building a Ramp requires that you:
  Pre-plan: Where is the best place? Do you need a building permit? How much will it cost? How much material? Plan for a 1:12 grade!
  A ramp should include these features:
    36” of width to accommodate the wheelchair/person
    Handrails, vertical uprights and a curb stop to keep all 4 wheelchair wheels on the ramp
    Start a ramp at a sidewalk or pavement and end it with a level landing at the building entry
    Create a non-slip surface: use shingles, adhesive strips, etc.
    Create a level spot for resting when you build a long ramp

## Slide 7: Well-designed Ramps

## Slide 8: Well-designed Ramps

## Slide 9: Well-designed Ramps

## Slide 10: Well-designed Ramps
House
Ramp
5’
5’
36”
Ramp Landing

## Slide 11: Well-designed Ramps
In this remodel, a 2-car garage was made into a wheelchair accessible apartment for someone with C-3,4 SCI injury. The ramp runs along the side of the house to the back and entry through the laundry/mud room. The ramp is hardly noticeable.

## Slide 12: Well-designed Ramps
From the front door, this ramp slopes down to the alley way and the garage where transfers occur!
A way to hide the extra ramp length needed to climb more than 5 steps at the front entry

## Slide 13: Some houses don’t need a ramp!

## Slide 14: Would you have done something different?

## Slide 15: Would you have done something different?

## Slide 16: Would you have done something different?

## Slide 17: Would you have done something different?

## Slide 18: Things to consider
Disguise or hide your ramp and keep it dry and snow free
Tuck it into a two-car garage with a ramp or a porch lift
Enter through the laundry, mud room or kitchen

## Slide 19: Garage Ramp
Garage Ramp with a switch back. It takes up one car space
Enter the garage with a garage door opener.

## Slide 20: Garage Ramp

## Slide 21: Rent a ramp for temporary use

## Slide 22: Things to consider
Two sets of hand rails - one at normal height, the other at wheelchair height
Maintain steps along with ramp!

## Slide 23: Things to consider
Ramps aren’t the only option
Consider a porch lift!
Can even climb up to a second story floor

## Slide 24: For here and there
Aluminum Ramps:
Threshold folding
Suitcase ramps

## Slide 25: For two stories
Home Elevator or Lifts
Dolphin Lift through the ceiling

## Slide 26: For two stories
Home Elevator or Lifts
Incline Platform lift

## Slide 27: Living Areas
Next, see examples of:
Ramps
Living Areas
Bathrooms
Kitchens
Outdoor Living

## Slide 28: Living Areas
Get rid of area rugs and create an open floor plan!
Remove and store extra furniture!

## Slide 29: Living Areas
Know doorway widths and the width of your wheelchair
  Most power chairs are 25” wide or less at powerbase
  Choose a mid-wheel drive
  Manual chairs are hip width + 4.5” on each side for wheels + push rims
Narrow hallways make it hard to complete turns into narrow doorways
Hallways 32” minimum

## Slide 30: Living Areas
A 5’ wide hallway makes it possible to complete a 180° turn and makes turns into rooms off the hallway easier
Protective materials or panels can be added to protect the hallway drywall.
Add kick-plates for doors
Use swing clear door hinges

## Slide 31: Living Areas
Swing Clear or Off-set door hinges take the thickness of the door out of the door width. This gives an extra 1-1.5” in the doorway.

## Slide 32: Living Areas
Lever-style door knobs make managing doors much easier for everyone… but especially someone with poor hand strength
Push button door locks eliminate keys

## Slide 33: Living Areas
Closets:
Adding wire shelves & drawers to a closet creates functional reach at wheelchair level
Adapting the Home: Living Areas

## Slide 34: Living Areas
Adapting furniture
Make it a better height for transfers
Put risers on legs to increase the height of desks, beds, tables, couches & arm chairs!
Adapting the Home: Living Areas

## Slide 35: Living Areas
An efficient computer desk and workspace
Adapting the Home: Living Areas

## Slide 36: Living Areas
Choose a height adjustable computer desk and workspace… motorized or not!
Adapting the Home: Living Areas

## Slide 37: Living Areas
A Bean Bag desk or laptop desk can make any location into a work space.
Adapting the Home: Living Areas

## Slide 38: Bathrooms
Next, see examples of:
Ramps
Living Area
Bathrooms
Kitchens
Outdoor Living

## Slide 39: Bathrooms
Bathroom plans can vary greatly base on user needs
Lets look at simple ones first

## Slide 40: Bathrooms
Grab bars and transfer poles can be very important
Single lever faucets are helpful

## Slide 41: Bathrooms
An accessible powder room can make a home “visitable”

## Slide 42: Bathrooms
There are many styles of grab bars & transfer aids

## Slide 43: Bathrooms
Shower Bench Choices:
Padded or not
Inside the tub or straddling it
Adjustable leg length
Back support or not
Just add a handheld shower wand

## Slide 44: Bathrooms
Shower Chair
A person sitting in this chair can complete a bowel/bladder program taking advantage of the cut-out seat and then roll directly into a shower
Order tilt in space if needed

## Slide 45: Bathrooms
A drop-in fiberglass shower unit can fit into the floor space previously used by a bath tub
Adapting the Home: Bathrooms

## Slide 46: Bathrooms
Roll in Showers
Can even be created in mobile homes
Transfers happen outside the bathroom
Greatly reduced effort for caregiver

## Slide 47: Bathrooms
Very functional
Open shelves are helpful for weak uppers
Shower head slides up & down
Lower the mirror

## Slide 48: Bathrooms

## Slide 49: Kitchen
Things to consider:
How much do you cook? Meals? Snacks? Reheat?
How far over the cabinet depth can you reach?
How high above your head can you reach?
How strong are your hands? Shoulders?
Do you have particular area of optimal function …like lap height? Or 6” lower than the counter top?
Let look at some ideas…

## Slide 50: Kitchens
Adding a lap length shelf to an existing island can create a good work surface with room for knees
Moving a microwave to the countertop makes it easier to use
Adapting the Home: Kitchen

## Slide 51: Kitchens
The kitchen sink may be a great place to start a kitchen re-do!
Lower only the sink
Buy a shallow sink
Install a lever faucet handle faucet
Roll the cabinet doors back inside the base unit
Adapting the Home: Kitchen

## Slide 52: Kitchens
Remove the floor of the base cabinet
Doors roll back into the cabinet frame
Supplies hang on swing-out doors and make room for knees
Don’t forget…Pipes should be wrapped or insulated to prevent burns
Adapting the Home: Kitchen

## Slide 53: Kitchens
A pull-out counter top is next to the wall oven
Note the dishes in slots

## Slide 54: Kitchens
Food and dish storage in deep pull-out drawers

## Slide 55: Kitchens
More ideas for storage

## Slide 56: Kitchens
Floating cook top with knee space,
Can also be ordered with a motor to raise and lower the height
Also has a handy pull-out counter top or cutting board

## Slide 57: Kitchens
Another approach…
Front controls on a non-gas stove are an important safety feature
Adapting the Home: Kitchen

## Slide 58: Kitchens
A kitchen remodeled with IKEA components… Notice the open shelving for storage and ease of access

## Slide 59: Kitchens
Totally remodel to make the perfectly accessible kitchen

## Slide 60: Here and there
Laundry Room make over. What else would you change?

## Slide 61: Here and there
Infant’s crib: Helpful when arms are weak. Changing table is adjacent.

## Slide 62: Here and there
Pool & Hot Tub lifts

## Slide 63: Here and there
Good news… the ADA requires that pools intended for pubic access must have a pool/hot tub lift!

## Slide 64: Bring photos or floor plans of your house!
Planning for Discharge:
Use your phone or tablet to capture layout of your home or apartment

## Slide 65: Get advice for your needs
Work with your OT and your family to get some specific advice based on your abilities, your home layout. At first, some changes will be more important than other changes

## Slide 66: Resources
Most adaptations to the home can be done with minimal expense. Call on handy friends or church members.
Compare renovation cost against nursing home care or cost of hiring a homemaker or personal care assistant.
Your OT can advise on your level of ability and which modifications are most important for safety & function.
Don’t forget to use: YouTube, Google, Pinterist
Look for: Free floor plans for homes & home additions, products, ideas, etc.
Low interest loans from Tech Act Projects, Vocational Rehab, VA Healthcare, some Medicaid, etc.